## Slide 1: AUTOMATIC METER READING

## Slide 3: INTRODUCTION
Automatic meter reading(AMR)is the collection of ,at a remote central location, data from consumption meters located at customer’s premises via tele communication links.
The meter could measure gas, water or electricity flow. These links could be Telephone lines, power line carrier communication(PLCC),Radio frequency CATV etc.
Automatic Meter Reading is a telephone-based, calling outbound system, for utility control and reliable, low-cost meter reading.
With the use of AMR, the need of person to visit the customer’s site and record the reading of the meter is eliminated. This also prevents human errors in recording the reading.

## Slide 4: How does the system work
The key to system is device called an ERT (Encoder- Reciever-Transmitter).
This device is connected directly to a special electronic register on the water meter.
Normally the ERT does nothing it “sleeps”, waiting for the meter reader to approach.
The meter truck-mounted reading the device sends out a continuous “wake up” signal.
When an ERT recieves the signal, it checks the reading on the meter register, encodes it into a digital signal, and begins transmitting its identification number and the current reading.
After a few minutes, the ERT stops transmitting and goes back to “sleep “. Waiting for the next time meter reading.
The truck-mounted computer system matches the ERT identification number with the property and records the reading. At the end of the day, the meter reader unloads the information to our billing system.
AMR also need meter interface unit(MIU). It responds to calls initiated through the software installed on a pc. A simple three-wire hook-up from the encoded register provides input from the meter to the MIU.

## Slide 5: AMR SYSTEM OVERVIEW
The remote AMR system is a host driven, multi-level network system consisting of a Host Central Station(HCS), Data concerntrator units(DCU) and meter Interfacing unit(MIU),with built-in flexibility and expandability.

## Slide 6: BENEFITS OF AMR TO UTILITIES
Reduced meter reading costs.
Ability to access difficult-to-read meters.
Improved customer service.
Reduced percentage of estimated bills.
Improved meter reader safety.
Implimentation of real-time pricing.
Distribution automation.
Improved fraud detection.

## Slide 7: AMR OVER CONVENTIONAL METER READING
Obtain more easily initial and final meter readins for closing accounts.
Streamline high bill investigations.
Help pinpoint system losses.
Help detect theft of service.
Enable more frequent readings with little incremental cost.
Enable custom billing dates.